## Slide 1
SK SET · CONCEPT PARTIS · REV 0.1 · AUG 2026
A-FRAME HYBRID
NORTHERN MICHIGAN
LAKEHOUSE
A-frame + 2-car under · lakeside deck · 20-ft container pool · one 3D-printed curved element
CONCEPT ONLY — NOT FOR CONSTRUCTION
Notes: Three partis, same program: A-frame with a 2-car under part of it, lakeside deck, 20-ft container pool, and one 3D-printed curved element. Target: inland lake, northern Michigan.

## Slide 2
RL LAKEHOUSE · SK-1 · REV 0.1 · 2026-08-14
SK-1
STACKED CHALET
NTS
Full A-frame riding on a walkout plinth — garage buried in the plinth on the road side, glass gable to the water. The plinth itself is the printed piece.
PARTI PLAN — LAKE UP
LAKE ELEVATION
WATCH-OUT
Needs 8–10 ft of grade fall to the water or the walkout dies. Buy the slope before you buy the scheme.
PROGRAM
Plinth: 2-car + mud/mech, lakeside walkout guest. Main: great room at the gable, kitchen mid, primary rear. Loft: 2 beds + bath. ≈2,300 sf living.
POOL
Parallel to shore, flush at the deck edge, on its own helical piles.
PRINTED PIECE
3DCP plinth — printed concrete, curved entry corner, layer lines left exposed.
CEDAR
BRONZE SEAM
BLACK RAIL
PRINTED CONC.
Notes: The first reference photo done as a bank house. Best fit for a sloped lot; the printed concrete plinth is the 3DP move.

## Slide 3
RL LAKEHOUSE · SK-2 · REV 0.1 · 2026-08-14
SK-2
A + BAR
NTS
Pure A-frame kept sacred — great room and loft only — beside a flat-roof bar carrying garage, beds, and a roof deck. The curved printed link is the hinge between the two languages.
PARTI PLAN — LAKE UP
LAKE ELEVATION
WATCH-OUT
Keep the bar clear of the A's snow-shed zone — the gap is avalanche avoidance, not just composition. Size the link roof for slide load.
PROGRAM
A-volume: double-height great room, loft primary. Bar: 2-car + entry at grade; 2 beds + bath over; roof deck on the lake end. ≈2,400 sf living.
POOL
Perpendicular to shore, in line with the bar — a third module. A MOONDOCK unit in residential trim.
PRINTED PIECE
Curved entry link — printed-mold GFRC panels or LFAM polymer rainscreen.
MATTE BLACK
TORREFIED ASH
WOOD SOFFIT
GFRC LINK
Notes: The AKAY container-hybrid parti from the second reference. Container pool reads as a third module of the same family.

## Slide 4
RL LAKEHOUSE · SK-3 · REV 0.1 · 2026-08-14
SK-3
KICKED RIDGE
NTS
Asymmetric A — one roof plane runs long over a drive-under garage; the lake-end eave kicks up in a curved glulam sweep over the deck. The curvature is real structure, not applied.
PARTI PLAN — LAKE UP
SIDE ELEVATION — LAKE AT LEFT
WATCH-OUT
The premium option — curved glulams + curved panels mean the longest fab lead times. Lock roof geometry early; everything references it.
PROGRAM
Grade: garage + entry under the tail. Main: great room to the lake gable, kitchen/dining mid. Loft: primary + bunk. ≈2,200 sf living.
POOL
Perpendicular off the deck corner, nose toward the water.
PRINTED PIECE
Curved gable-end + eave fascia panels following the glulam sweep — printed molds to GFRC, or LFAM polymer.
ZINC ROOF
LARCH
BLK STEEL
GFRC PANELS
Notes: Closest to the last two references. Most sculptural, most fab-intensive; the curve is structural glulam with printed panels following it.

## Slide 5
RL LAKEHOUSE · NOTES · REV 0.1
NORTHERN MICHIGAN · 45TH PARALLEL
REALITY CHECKS
60–70+ psf
SNOW
Ground snow up north. A-frames shed to the two long sides — decks, walks, garage doors, and the pool stay at the gable ends. All three partis are drawn that way.
≈50,000 lb
POOL STRUCTURE
A 20-ft container pool, full. Never on deck framing — own helical piles with a flush-deck surround. Insulate + heat pump for May–Oct; drain down after.
40–75 ft
SITE + ZONING
Typical inland-lake OHWM setbacks, township-specific; pools usually count as structures. Frost footings 42–60 in. Septic + well drive siting as much as the view.
R302.6
GARAGE UNDER
Dwelling separation at the garage lid and shared walls per the Michigan Residential Code. Cheap now, annoying in a retrofit.
Notes: Numbers are concept-level; confirm ground snow, setbacks, and frost depth with the specific township once the parcel is real.

## Slide 6
RL LAKEHOUSE · NOTES · REV 0.1
THREE BUILDABLE ROUTES
THE PRINTED PIECE
A
3DCP PLINTH / SITE WALLS
Printed concrete, on-site or precast. Citizen Robotics in Detroit is the obvious first call — keep the fab local.
BEST FIT: SK-1
B
PRINTED MOLDS → GFRC
Print the formwork, cast glass-fiber-reinforced concrete panels. The most freeze-thaw-proven route to curved facade geometry.
BEST FIT: SK-2 / SK-3
C
LFAM POLYMER RAINSCREEN
Large-format printed panels hung on conventional framing. Lightest and fastest to iterate — verify UV + thermal-cycling specs first.
FASTEST TO PROTOTYPE
Notes: One curved element, three fab paths. GFRC from printed molds is the safest bet for a four-season lakefront; 3DCP is the boldest if the plinth is the move.

## Slide 7
RL LAKEHOUSE · WORKFLOW · REV 0.1
CONCEPT TO NATIVE RVT + FAB EXPORT
PATH TO REVIT
1
FORMA
Drop the actual parcel in — massing, sun, wind + snow, and view corridors before committing to a parti.
2
CONCEPTUAL MASS
Winning parti into Revit; generate walls, floors, and roofs by face.
3
ADAPTIVE COMPONENT
The printed element stays parametric — adaptive family or Dynamo-driven surface.
4
STEP / OBJ OUT
Fab geometry exports straight to the printer; everything else stays native RVT.
FORMA MASSING FIRST — THE PARCEL PICKS THE PARTI BEFORE TASTE DOES.
Notes: Same discipline as the TEG pipelines: parametric where it pays, native everywhere else.

## Slide 8
NEXT REV
PICK A PARTI.
Rev 0.2 develops the winner: plans, sections, and a Forma-ready massing brief.
SK-1 lives or dies on 8–10 ft of grade fall to the water — let the lot vote before taste does.
CONCEPT ONLY — NOT FOR CONSTRUCTION
Notes: If the parcel isn't locked yet, run all three partis through Forma on the shortlist lots — slope and shore orientation will eliminate at least one for free.